## Slide 1
Parametric Study on Structural Efficiency and Economy of Transmission Towers.
Name: Nallajarla Siva Rama Krishna
Roll no: CE24M309
Department of Civil and Environmental Engineering,
Structural engineering
Indian Institute of Technology Tirupati.
SEMINAR ONE PRESENTATION.

## Slide 2
5. Reference.
Table of content.
1. Intro.
4. Conclusion.
3.3 Base width.
3.4 Bracings system.
3.1 Sections.
3.5 Codes design.
3.2 Configuration.
1.1 - Types of transmission towers.
1.2 - Loads on transmission towers.
3. Parametric study.
2. Objective.

## Slide 3
Electric Power Transmission and Distribution Layout.
1.1 - ABOUT THE TRANSMISSION TOWER.
Transmission towers (electrical pylons) carry high-voltage electricity over long distances.
Typical heights range from 50-150 ft (16-45 m) and tallest reach 1,247 ft (380 m).
They connect power plants to substations, linking different grid regions.
Transmission line towers form a major component of the power transmission network, contributing nearly 30 to 40% of the overall project cost.
Inefficient design may lead to excessive deflection, higher steel consumption or increased cost.
Most towers are made of steel, while some use concrete, wood or ductile iron.
1. Intro.
2. Objective.
4. Conclusion.
3. Parametric study.
5. Reference.
https://www.eia.gov/energyexplained/electricity/delivery-to-consumers.php

## Slide 4
Types of transmission towers
a) Single circuit tower
b) Double circuit tower
c) Multi circuit tower.
Based on circuit
a) Lattice Structure
b) Hybrid Structure
c) Tubular Pole Structure.
Structure type
Current capacity
a) 11 kV,
b) 33 kV
c) 66 kV
d) 110 kV
e) 132 kV
f) 220 kV
g) 400 kV
h) 500 kV
Material used
a) Steel Structure
b) Wooden Material
c) RCC Pole
Based on angle
a) A – type tower – angle of deviation 0o to 2o.
b) B – type tower – angle of deviation 2o to 15o.
c) C – type tower – angle of deviation 15o to 30o.
d) D – type tower – angle of deviation 30o to 60o.
e) E – type tower – angle of deviation 60o to 90o.
Force applied by the conductor on the cross arms
Tangent suspension tower
Angle tower or tension tower
1. Intro.
2. Objective.
4. Conclusion.
3. Parametric study.
5. Reference.

## Slide 5
1. Intro.
2. Objective.
4. Conclusion.
3. Parametric study.
5. Reference.

## Slide 6
Guyed mast tower at north of IIT Tirupati.
www.savree.com/en/encyclopedia/electrical-transmission-towers
1. Intro.
2. Objective.
4. Conclusion.
3. Parametric study.
5. Reference.

## Slide 7
Minimum permissible ground clearance (H1).
Maximum sag of overhead conductor (H2).
Vertical spacing between the top and bottom conductors (H3).
Vertical clearance between the ground wire
and top conductor (H4).
https://www.electrical4u.com/electrical-transmission
Fig. - Nesting platform for bird nesting.
1. Intro.
2. Objective.
4. Conclusion.
3. Parametric study.
5. Reference.

## Slide 8
To decide the efficient code for tower design.
To select the efficient bracing configuration.
To select the effective base width for the different wind zones.
To select the best sections out of angle and hollow tube sections.
To select the efficient configuration (VCT and HCT) of towers.
1. Intro.
2. Objectives.
4. Conclusion.
3. Parametric study.
5. Reference.

## Slide 9
Parameters.
Bracing
Base width
Configuration
Sections
Codes
K type
X type
Diagonal
XD
Combined
In different wind zones :-
Z-1
Z-2
Z-3
Z-4
Z-5
Z-6
Vertical
Horizontal
Angular
Tubular
Is 802
Is 800
AISC
EN
1. Intro.
2. Objective.
4. Conclusion.
3. Parametric study.
5. Reference.

## Slide 10
5.1 - SECTIONS COMPARASION[1].
1. Tower Specifications.
2. Tower Analyses.
4. Soft ware Used
3. Loads Considered.
Self-weight (Dead load)
Conductors & Hardware load
Wind load on tower and conductors
Ice/Snow load (if applicable)
Earthquake/Dynamic load
Load combinations for extreme conditions
Type - | Four legged suspended tower of 400 KV double circuit.
Height - | 40 m.
Sections - | Angle and closed hollow section.
Configuration- | X-Bracing and K-Bracing Patterns.
Linear Static Analysis.
Dynamic analysis.
STAAD Pro for 3D modeling and analysis.
One broken wire and anti-cascading condition.
Indian code is 802 part1.
Cont.
(IJAERD), vol. 4, 2017.
Fig - Four legged suspended tower.
1. Intro.
2. Objective.
4. Conclusion.
3. Parametric study.
5. Reference.

## Slide 11
6 - RESULTS.
Fig. - Deflections for various sections.
Chart: Deflection (mm) graph
| Angle section (mm) | Closed hollow section (mm)
Wind load | 85 | 75
Earthquake load | 65 | 68
83.2
Chart: Cost (Rs.)
| Angle section | Closed hollow section
Cost (Rs.) | 1500000 | 1250000
5 - Parameters used to decide which section is better.
Structural Deflection.
Economy (Weight and Cost).
Permissible Limits Check.
Fig - Costs for various sections.
Cont.
65
75
68
15,00,000
12,50,000
1. Intro.
2. Objective.
4. Conclusion.
3. Parametric study.
5. Reference.

## Slide 12
7 - Observations.
Best section was concluded as the four-legged transmission tower with “Closed Hollow Sections” since it was both structurally stiffer and more economical.
8 - Reasons.
9 - Challenges with Hollow Sections.
1. Intro.
2. Objective.
4. Conclusion.
3. Parametric study.
5. Reference.

## Slide 13
5.2 - CONFIGURATION TYPES[2].
1. Tower Specifications.
2. Tower Analyses.
Soft ware Used
3. Loads Considered.
Self-weight (Dead load)
Conductors & Hardware load
Wind load on tower and conductors
Ice/Snow load (if applicable)
Earthquake/Dynamic load
Type - | 132 kV double circuit self-supporting angle tower.
Height - | HCT = 38.83 m & VCT = 44.85m
Span - | 200 m
Base Width - | 7.6 m for both VCT and HCT.
Material - | Mild steel and High tensile steel.
Configuration- | Vertical Configured Tower and Horizontal configured tower.
Linear Static Analysis.
STAAD Pro for 3D modeling and analysis.
VCT
HCT
1. Intro.
2. Objective.
4. Conclusion.
3. Parametric study.
5. Reference.

## Slide 14
4. GRAPHS.
Cont.
Chart: Comparison of tower weights and wind loads (HCT and VCT).
| Weight (kg) | Wind Load (kg)
VCT | 6800 | 11500
HCT | 6200 | 10000
Chart: Maximum force in bracing members.
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
VCT Compressive (kg) | 9000 | 10500 | 13500 | 16500 | 21000 | 22000 | 21000 | 24000 | 21500 | 13500 | 11000 | 12000 | 12000 | 5000
VCT Tensile (kg) | 11000 | 14000 | 18000 | 22000 | 27000 | 23000 | 14000 | 15000 | 13000 | 4500
HCT Compressive (kg) | 10500 | 13000 | 17000 | 21000 | 27000 | 23000 | 14000 | 15000 | 13000 | 4500
HCT Tensile (kg) | 11000 | 13500 | 17500 | 22000 | 26500 | 13000 | 14000 | 13000 | 4500
1. Intro.
2. Objective.
4. Conclusion.
3. Parametric study.
5. Reference.

## Slide 15
5. OBSERVATIONS.
6. REASONS.
Choose between weight and cost savings.
Vertical vs Horizontal Configuration.
1. Intro.
2. Objective.
4. Conclusion.
3. Parametric study.
5. Reference.
HCT

## Slide 16
5.3 - BASE WIDTH COMPARASION[3].
1. Tower Specifications.
2. Tower Analyses.
4. Soft ware Used
3. Loads Considered.
Self-weight (Dead load)
Conductors & Hardware load
Wind load on tower and conductors
Ice/Snow load (if applicable)
Torsional & Longitudinal wind effects
Type - | Self-supporting lattice steel transmission tower
Height - | 34.120 m
Top width - | 0.5 m
Base Width - | 6.307 m
Cross arm length - | 9.2 m
Material - | Steel (Fe415)
Sections used - | ISA
Linear Static Analysis: For base comparison under normal loads.
STAAD Pro for 3D modeling and analysis.
1. Intro.
2. Objective.
4. Conclusion.
3. Parametric study.
5. Reference.

## Slide 17
5.1 Graph between k values and base widths for 34.120m and 55m heights.
5.2 Graph between k values and height to width ratios for 34.120m and 55m heights.
5.3 Graph between base widths and k values for 34.12m height.
5.4 Graph between base widths and (weight/length) values for 34.12m Height.
5. GRAPHS.
Cont.
1. Intro.
2. Objective.
4. Conclusion.
3. Parametric study.
5. Reference.

## Slide 18
Cont.
7. REASONS.
Optimum Stability vs. Economy:
Wider bases improve tower stability and reduce deflection under wind loads.
2. Height-to-Base Ratio (h/b = 3.79):
This ratio ensures adequate stiffness while keeping the tower design economical.
3. Wind Zone Adaptability:
Base widths are chosen to suit different wind zones, increasing slightly for higher wind speeds.
This provides better resistance to lateral loads without overdesigning for low-wind areas.
1. Intro.
2. Objective.
4. Conclusion.
3. Parametric study.
5. Reference.
6. OBSERVATIONS.
9 m for 34.12 m tower (k = 0.45).
14.5 m for 55 m tower (k = 0.345).
Towers in higher wind zones (Zone IV) require slightly wider bases for the same height compared to Zone II.

## Slide 19
5.4 - BRACING COMPARASION[4].
1. Tower Specifications.
3. Tower Analyses.
Soft ware Used
2. Loads Considered.
Dead Load, Wind Load, Longitudinal Load, Vertical Load, Seismic Load, Temperature Load and Dynamic Load.
Type - | Self-supporting lattice tower.
Height - | 27 m – 55 m (up to 75 m for 500 kV).
Height range - | 27 m – 55 m (up to 75 m for 500 kV).
Base Width - | 4 m – 10 m (varied for optimization).
Material - | 
Configuration- | K, X, Diamond (D), Single Diagonal, Cross-Diagonal, KD, Y, YD, XBX, Pratt, KX.
Linear and non linear Static Analysis.
STAAD Pro for 3D modeling and analysis
4. Bracing considered.
1. Intro.
2. Objective.
4. Conclusion.
3. Parametric study.
5. Reference.

## Slide 20
5. GRAPHS.
Radar graphs.
Cont.
Chart: Overall Efficiency of Bracing Systems.
| X | K | D | KD | YD | XB | XBX
Weight | 1.05 | 1.03 | 1 | 1.04 | 1.02 | 0.9 | 0.95
Deflection | 1.15 | 1.4 | 1.3 | 1.25 | 1.35 | 1.2 | 1.3
Stiffness | 1 | 0.95 | 1.05 | 1.1 | 1.05 | 1.15 | 1.1
Economy | 1 | 0.75 | 0.9 | 0.95 | 0.85 | 0.7 | 0.8
Performance | 1 | 0.8 | 0.95 | 0.9 | 0.85 | 0.75 | 0.85
Chart: 
| K | KD | Y | YD | D | XB | X
Weight (N) | 74000 | 61000 | 88000 | 62000 | 63000 | 145000 | 123000
Chart: sway comparison of 60 m tower (cm).
| K | KD | Y | YD | D | XB | X
Out of Plumb (cm) | 64 | 68 | 62 | 64 | 67 | 54 | 52
1. Intro.
2. Objective.
4. Conclusion.
3. Parametric study.
5. Reference.

## Slide 21
Bracing configuration governs both economy and stiffness.
X-bracing generally yields minimum weight and uniform force distribution.
K-bracing offers higher stiffness but adds steel.
Diamond (D) and Cross-diagonal are good compromises.
KD/YD suitable for telecom towers (tall, slender).
Bracing | Structural Behaviour | Reason for Efficiency
X-Bracing | Direct tension–compression path; symmetrical load transfer. | Minimum deflection & weight → most economical.
D / Diamond | Secondary diagonal reduces unbalanced forces. | Stable, uniform stress distribution.
K-Bracing | Redundant members, higher stiffness. | Lower deflection but heavier; useful in high-wind zones.
KD / YD | Combined K & diagonal system. | Good economy for tall slender telecom towers.
XBX / Cross-Diagonal | Multiple load paths. | Balanced between stiffness & weight.
6. OBSERVATIONS.
7. REASONS.
1. Intro.
2. Objective.
4. Conclusion.
3. Parametric study.
5. Reference.

## Slide 22
5.5 - CODE COMPARASION[5].
1 Tower Specifications.
3 Tower Analyses.
4 Soft ware Used
2 Loads Considered.
Self-weight (Dead load)
Conductors & Hardware load
Wind load on tower and conductors
Ice/Snow load (if applicable)
Torsional & Longitudinal wind effects
Earthquake/Dynamic load
Cyclonic (gust) load factors (IS 875 Part 3: 2015)
Load combinations for extreme conditions
Type - | 220 kV Double-Circuit Lattice Tower
Height - | 40 m
Span - | 200 m
Base Width- | 5.95 m (Square Base)
Material- | Equal-Angle Steel Sections (Mild and High-Tensile Steel)
Configuration- | X-Bracing and K-Bracing Patterns
Linear Static Analysis - For base comparison under normal loads.
Dynamic Analysis - Time-dependent and seismic response.
STAAD Pro for 3D modeling and analysis
ANSYS for validation and parametric optimization
1. Intro.
2. Objective.
4. Conclusion.
3. Parametric study.
5. Reference.

## Slide 23
5 - GRAPHS.
Cont.
1. Intro.
2. Objective.
4. Conclusion.
3. Parametric study.
5. Reference.
Chart: Buckling curve comparison
| 0 | 0.25 | 0.5 | 0.75 | 1 | 1.25 | 1.5 | 1.75 | 2
IS 800 | 1.02 | 0.95 | 0.8 | 0.65 | 0.53 | 0.43 | 0.36 | 0.3 | 0.26
IS 802 / ASCE | 1.03 | 0.96 | 0.83 | 0.7 | 0.57 | 0.46 | 0.38 | 0.32 | 0.28
BS EN | 1.05 | 0.97 | 0.84 | 0.72 | 0.59 | 0.48 | 0.4 | 0.34 | 0.3
Chart: Deflection vs Wind speed
| 20 | 30 | 40 | 50 | 60 | 70
IS 802 | 0.16 | 0.25 | 0.34 | 0.44 | 0.54 | 0.65
IS 875 | 0.17 | 0.27 | 0.37 | 0.5 | 0.61 | 0.73
ASCE | 0.18 | 0.28 | 0.38 | 0.49 | 0.6 | 0.72
BS EN | 0.14 | 0.22 | 0.28 | 0.36 | 0.44 | 0.52
1
2

## Slide 24
Wind load is the most critical factor in tower design, especially in cyclone-prone regions.
IS 802 (2015) needs revision to include k₄ factor for cyclonic safety (as adopted in IS 875 (2015)).
IS 802 (2015) is adequate for normal zones but unsafe in coastal Wind Zone 5 without modification.
ASCE 10-97/10-15 and BS EN 1993-3-1 give more accurate and reliable load estimations for extreme winds and slender members.
Best Performing Code: IS 875 (Part 3): 2015 + ASCE 10-15 combination (or IS 802 revised with k₄ factor = 1.3).
Reasons:
  Accounts for cyclonic gust effects via importance factor (k₄).
  Harmonized with international reliability-based design methods.
  Produces safe, economical, and performance-based results in high wind zones.
  Reflects current understanding of fluctuating and directional wind loading on lattice towers.
6 - OBSERVATIONS
7 - Recommended / Best Code and Reasons.
1. Intro.
2. Objective.
4. Conclusion.
3. Parametric study.
5. Reference.

## Slide 25
1. Efficient bracings.
2. Efficient section.
3. Efficient configuration.
X-bracing offers the most efficient balance of stiffness, strength, and economy by uniformly distributing loads and minimizing deflection. Compared to K, Diamond, and KD patterns, it ensures greater stability with lower steel consumption, making it the most suitable choice for transmission tower design.
Closed hollow sections are more efficient than traditional angle sections, offering higher stiffness and lower deflection under wind and seismic loads. Despite slightly complex fabrication, they provide superior strength-to-weight performance and improved overall structural efficiency.
The horizontal configuration (HCT) is the most economical and practical design, offering stable performance with lower wind loads. Although slightly heavier, it allows the use of mild steel instead of high-tensile steel, resulting in significant cost savings.
1. Intro.
2. Objective.
4. Conclusion.
3. Parametric study.
5. Reference.

## Slide 26
4. Efficient code for design.
5. Efficient base width.
The optimum base width depends on tower height and wind zone, balancing both stability and economy. An ideal height-to-width ratio maximizes structural efficiency while minimizing excess steel and cost about 9 m for 34.12 m towers and 14.5 m for 55 m towers offer the best performance.
The IS 875 (Part 3): 2015 + ASCE 10-15 combination ensures safe and economical tower design by incorporating the k₄ factor for cyclonic and directional wind effects. A revised IS 802 with k₄ = 1.3 is essential for achieving reliable performance in coastal and high-wind regions.
1. Intro.
2. Objective.
4. Conclusion.
3. Parametric study.
5. Reference.

## Slide 27
[1] Comparative Study of Four-Legged Lattice Transmission Tower Having Angle and Hollow Sections, International Journal of Advance Engineering and Research Development (IJAERD), vol. 4, 2017.
[2] Analysis and Design of Vertical and Horizontal Configurations of Cross-Arms in a Transmission Line Tower, IJERT, vol. 4, 2015.
[3] M. N. Shyamenahalli and C. D. M. Determination of Economic Base Width of Transmission Tower for Different Wind Zones, International Journal of Research in Engineering and Science (IJRES), vol. 9, 2021.
[4] Abdulaqder M. Tah, Kamiran M. Asilevani, & Mustafa Özaçka. (2017). Comparison of Various Bracing System for Self-Supporting Steel Lattice Structure Towers. American Journal of Civil Engineering.
[5] Harsha Jatwa, Vivek Tiwari, & Sumit Pahwa. (2017). Comparative Study of Indian and ASCE Codes Provision for Design of Transmission Tower. International Journal of Innovations in Engineering and Technology (IJIET), vol. 9.
1. Intro.
2. Objective.
4. Conclusion.
3. Parametric study.
5. Reference.

## Slide 28
THANK YOU
The Land of Giants.
By Choi+Shine Architects (south Korea).